## Slide 1
Tristan Traiber – 22.02.2022 – MSE – EIE - TIN
TM Project Defense
Analog LTE-M / NB-IoT Watch

## Slide 2
TM Project Defense - Analog LTE-M / NB-IoT Watch
Table of contents
  Introduction
    Project Description
    Scope & Limitation
  Literature Review & Research
    Wearable & Low-Power App
    System MCU (nRF9160 SiP)
    System Power Supply
    Cellular IoT & GNSS
  Results & Solutions
    Specification
    Functional Decomposition
    Component Selection
  Hardware Part
    Electrical Schematic
    LTEWatch Prototype Board
  Antenna Part
    Cellular (LTE-M/NB-IoT)
    GNSS
  Software Part
    LTEWatch Application Decomposition
    LTEWatch Application Diagram
    Software Architecture
    External Library
    Hardware Description
  Test & Result
    LTEWatch Device
    GNSS & LTE-M/NB-IoT
  Discussion
    Personal Evaluation
    Remaining Work
  Conclusion

## Slide 3
Introduction
Project Description
  About Nordic Semiconductor
    Fabless Semiconductor Company from Norway
    Specialized in wireless communication technologies and IoT
    Pioneer role in development of Bluetooth Low Energy (BLE)
    Currently developing for ANT+, Thread, Zigbee, LTE-M/NB-IoT, Wi-Fi and GSMA
  Goals & Objectives
    Develop an analog wristwatch with cellular LTE-M/NB-IoT communication and GNSS position tracking using Nordic’s nRF91 family of devices.

## Slide 4
Introduction
Scope & Limitation – Task List
  Specification
    Elaborate the specification of the device (number of clock hands, battery lifetime, user interface, size, recharging mechanism, case)
  Antenna
    Study and implement antenna solutions for both GNSS and LTE-M/NB-IoT
  Hardware
    Component selection
    Design of the schematic and PCB of a prototype
    Assembly and electrical testing of the prototype
  Software
    Develop a simple watch application that must implement motorized clock’s hands, buttons, LCD, LTE-M/NB-IoT communication using the MQTT protocol, GNSS position and time tracking, battery charging and level monitoring, accelerometer.
  Prototype validation
    Test and validation of the entire development
  Documentation
    Establish a technical report enabling further developments

## Slide 5
Introduction
Scope & Limitation – Project Constraint
  Limited Time (20 weeks)
    Too limited to develop a complete product solution
    Focus on the development of a proof of concept (POC)
    Develop the system architecture and validate the hardware solution as well as the software implementation capability
    Prefer good, reliable and simple solutions to perfect, complex and risky solutions
  Limited Resourses
      Prefer smart and economical solutions
    Require to sacrifice some optimization against the availability and accessibility of the solution
    Keep solution as versatile as possible for further improvement or modification
    Avoid customized or overly specific solutions as much as possible to minimize dependency to suppliers and current market situation

## Slide 6
Literature Review & Research
Wearable & Low-Power application’s constraints considerations
  Mechanical
    Portability: Increase component density and decrease weight by using more expensive fully integrated components
    Ergonomics: Increase size and accessibility of user interface (touchscreen)
  Price and availability
    Ease of production: Number of components and system complexity
  Performance
    Battery life: Reduce wasted power by using more efficient components
    Thermal dissipation: Ultra-compact
    Charging time: Maximum charging current capability
  Quiescent current (IQ)
    Current drawn by an active IC
    When in non-switching (stable) and a no-load (disconnected) configuration

## Slide 7
Literature Review & Research
System MCU (nRF9160 SiP)
  Multimode LTE-M/NB-IoT modem
    700-2200 MHz LTE band
    +23 dBm output power
    eDRX and PSM power saving features
    Single pin 50 Ω antenna interface
    UICC interface (SIM/eSIM)
  Application processor and memory
    64 MHz Arm® Cortex®-M33 CPU
    Arm TrustZone® for trusted execution
    Arm CryptoCell 310 (App. Lay. Security)
    1 MB Flash & 256 KB RAM
Application Circuit - nRF9160 SiP Product Brief

## Slide 8
Literature Review & Research
System Power Supply
  Power Supply Source
  Input Supply Protection
  Battery Manager
    Battery Charger
    Battery Protection
    Power Source Switch
  System Supply Manager
  Battery Level Monitoring
  Power Supply Indicator
  System Supply Measure/Switch
1
4
2
3
5
6
7

## Slide 9
Literature Review & Research
Cellular IoT
  LTE (Long-Term Evolution)
    Wireless broadband communication and data terminals standard (Mobile devices)
    Based on GSM/EDGE and UMTS/HSPA
    Bandwidth: 20 MHz
  LTE-M (Machine Type Communication)
    LTE low-power equivalent machine to machine communication standard
    Bandwidth: 1.4 MHz
    Lower throughput: ~100 kbit/s
    Longer range than LTE
  NB-IoT (Narrowband IoT)
    Drastically narrower bandwidth (200kHz)
    Longer range than LTE-M
    Lower throughput: ~30 kbit/s
  MQTT (Telemetry Transport)
    Machine to machine network protocol
    Publish–subscribe messaging pattern intended for message queue and message queuing service
    Run over ordered, lossless and bidirectional connections transport protocol (TCP/IP)

## Slide 10
Literature Review & Research
Global Navigation Satellite System (GNSS)
  Definition
    Satellite constellation providing PNT* services on a global or regional basis.
    Main PNT services
    BeiDou (BDS): People’s Republic of China (PRC) - 30 satellites
    Galileo: European Union - 30 satellites
    GLONASS: Russian Fed. - 24 satellites
    1. Positioning (P)
    2. Navigation (N)
    3. Timing (T)
    IRNSS/NavIC: India - 7 satellites. IRNSS (Autonomous system to cover India)
    QZSS: Japan (Operated by QZS System Service Inc. (QSS)) - 5 satellites

## Slide 11
Results & Solutions
System Specification
  Power supply
Must be powered by battery
    Must be rechargeable by USB-C and WPC
    Must have battery life of at least 24h
  Data display
    Time must be displayed with three mini stepper motors
    Must implement LCD screen
  Computing unit (MCU)
    Must implement the nRF9160 from Nordic
  User interface
    Must implement buttons as user interface
    An accelerometer can be added
  Radio frequency (RF)
    Must implement a GNSS receiver
    Must implement LTE-M/NB-IoT transceiver
    Must implement on-board antenna for both GNSS and LTE-M/NB-IoT
    Must have SMA connectors for external antenna for GNSS and LTE-M/NB-IoT

## Slide 12
Results & Solutions
Functional Decomposition
  System Functional Block Decomposition
    Power Supply Block
    User Interface Block
    Data Display Block
    RF Communication Block
    MCU & Programming Block
RF Com.
Power Supply
MCU & Prog.
Data Display
RF
User Interface

## Slide 13
Results & Solutions
Component Selection - Overview
  Power Supply
Li-ion/LiPo Battery Charger : Ti BQ25180
    Buck Boost Converter (+3V3) : Ti TPS63036
    LDO Regulator (+1V8) : Ti TPS7A03
    Wireless (WPC/QI) Receiver : Ti BQ51013B
  Computing Unit (MCU)
    System MCU : Nordic Semi. nRF9160
  User Interface
    USB To UART Interface : FTDI Chip FT234XD
  Data Display
    LCD Display : SHARP LS011B7DH03
    Motors : TITAN T901A/T902
  User Interface
    Accelerometer : mCube MC3635
  Radio Frequency (RF)
    GNSS Receiver : u-blox MAX-M10S
    GNSS Antenna : Ignion NN03-320
    LTE-M/NB-IoT Antenna : P822602 (Universal Broadband FR4 Embedded LTE/LPWA Ant.)

## Slide 14
Results & Solutions
Power Supply – Battery Charger
  Settings
Fully programmable by integrated I2C serial bus
  Consumption
  System Protection
Thermal reg. & shutdown
Watchdog & safety timer
Input OVP : 25V
  Battery Protection
FET Power Path
Battery thermal protection
Battery short protection
Charge and discharge current limit (1.1 / 2.5 A)
Battery UVP & OVP
  Size & Package
8-pin DSBGA (1.6×1.1)
Shutdown | Ship | Battery | Sleep
15 nA | 3.2 µA | 3 µA | 30 µA
Simplified Schematic - BQ25180 datasheet

## Slide 15
Results & Solutions
Power Supply – Buck Boost Converter (+3V3)
  Performances
Input voltage from 1.8V to 5.5V
Adjustable output voltage from 1.2V to 5.5V
High efficiency over entire load range
  Consumption
Low operating quiescent current : 25 µA
Power saving mode available
  Safety & Protection features
Thermal protection
Over-voltage protection
Load disconnect during shutdown
  Size & Package
8-pin WCSP package (1.814 mm × 1.076 mm)
  Efficiency
> 90% : 1.5 mA < ILoad < 300 mA
> 80% : 1.5 µA < ILoad < 800 mA
Application Circuit - TPS63036 datasheet

## Slide 16
Results & Solutions
Power Supply – Wireless Power Receiver (WPC)
  Specification & performances
Overall peak AC-DC efficiency: 93%
WPC v1.2 compliant communication control
Output voltage conditioning & input voltage up to 20V
  Control and safety features
Thermal shutdown protection
Rectifier over-voltage clamp with low-power dissipation (15V)
Control pin for temp. monitoring, charge complete & host check
  Size & package
VQFN 20-Pin : 4.5 mm × 3.5 mm
DSBGA 28-Pin : 3.0 mm × 1.9 mm
« Dual Power Path » Application Circuit - BQ51013B datasheet

## Slide 17
Results & Solutions
User Interface - Accelerometer
  Range, Sampling and Power
±2/4/8/12/16g ranges up to 10’000g
8/10/12-bit FIFO or 14-bit single samples
14...1300 sample/s (Intern. OSC / CLK Pin / SOFT)
Sniff and Wake modes (0.4 µA Sniff current, 6 Hz)
Ultra-Low Power 32 samples FIFO
  System Integration
I2C interface : ≤ 1 MHz
SPI Interface : ≤ 4 MHz
Single-chip 10p (Silicon MEMS) 1.6×1.6×0.94 mm
Low noise to 2.3 mg (RMS)
Typical 4-wire SPI Application Circuit – MC3635 Datasheet
25 Hz | 50 Hz | 100 Hz | 1.3 kHz
0.9 µA | 1.6 µA | 2.8 µA | 36 µA

## Slide 18
Results & Solutions
Data Display – LCD Screen
  Performances and Image Quality
Reflective monochrome TFT-LCD
1.08” diagonal & 160×68 resolution
Polarized anti-glare front surface
Refresh rate range up to 70 Hz
  Power Consumption
Breakout Board (nice!view)
Pinout and Schematic
MODE | TYP | MAX
Hold (Black) | 15 µW | 50 µW
Update (1Hz) | 25 µW | 100 µW
  Controls and Interfaces
10-Pin flat cable FPC type connector
3-wire SPI serial data signal (≤ 1MHz)
Integrated data storage of 1 bit/px
Arbitrary line data write mode
  Mechanical Properties
Compact, thin & lightweight monolithic construction panel
Outline dimension 32×14×0.745 mm

## Slide 19
Results & Solutions
Data Display – Motors
  Performances and Image Quality
Reflective
  Power Consumption
Breakout Board (nice!view)
Pinout and Schematic
MODE | TYP | MAX
Hold (Black) | 15 µW | 50 µW
Update (1Hz) | 25 µW | 100 µW

## Slide 20
  Description
Ultra-low-power M10 platform with extremely good performances for all L1 GNSS systems
  Performance
Consumption in cont. tracking mode: < 25 mW
↗ Position availability : concurrent reception of (GPS, GLONASS, Galileo and BeiDou)
↗ Reliability in challenging conditions (urban)
  Super-S Technology (u-blox)
Excellent sensitivity with small antennas
+25% of dyn. position accuracy (non-line-of-sight)
  Integrated Features
LNA & SAW filter : ↗ sensitivity (passive antenna)
Provide advanced spoofing and jamming detection
  Size & Package
Pin-to-pin compatibility with previous generations (MAX-6, MAX-7 & M8)
Size : 10.1 mm × 9.7 mm
Results & Solutions
RF – GNSS Receiver - Overview
MAX-M10S Data Sheet
Parameter | GPS+GAL | GPS + GAL + GLO | GPS + GAL + BDS B1I | GPS + GAL + BDS B1C | GPS + GAL + GLO + BDS B1C
Update rate (max) | 10 Hz | 10 Hz | 10 Hz | 10 Hz | 10 Hz
Position accuracy | 1.5 m | 1.5 m | 1.5 m | 1.5 m | 1.5 m

## Slide 21
MAX-M10S Module
Results & Solutions
RF – GNSS Receiver – Functional Diagram
MAX-M10S Data Sheet

## Slide 22
Antenna Part
Cellular (LTE-M/NB-IoT)
  On Board LTE-M/NB-IoT Antenna
    P822602 (Universal Broadband FR4 Embedded LTE/LPWA Ant.)
    Based on the nRF9160DK board
  Watch Strap Antenna
    Functional 800 MHz Dipole Antenna
    Easy and cost-effective RF solution
    Connection between antenna and device is the weak point

## Slide 23
Antenna Part
GNSS – Antenna Basics
  General Considerations
    Sky visibility : ↗ satellites = ↗ accuracy
    Strongest satellite :
  Active vs Passive Antenna
  Available Solution
    Patch Antenna
    Helix Antenna
    Chip Antenna
    PCB Antenna
    Fractal Element Antenna (FEA)
    Loop antenna
    Planar Inverted F Antenna (PIFA)
    High-end GNSS antennas
Active antenna | Passive antenna
↗ power (10-60 mW) | Does not add to power budget
More tolerant to minor impedance miss-match or cable length | RF line max length & design is critical (max length = 10 cm)
Keep receiver noise figure low | Sensitivity to jamming signals coupled to the RF line
Less affected by jamming signals (if equipped with filter) | RF design experience is required to properly design a passive antenna
Monopole Antenna
Dipole Antenna

## Slide 24
Antenna Part
GNSS – Patch vs Chip Antenna
  Patch Antenna
    Most common antenna for GNSS
    Ideal for flat surface mounting
    Low cost
    Very high gain capable
    Size range (40 × 40 mm to 10 × 10 mm)
    Require a large ground (min. 50 × 50 mm)
    Smaller antenna = lower overall gain
    Amplifying the signal after the antenna will not improve the SNR
  Chip Antenna
    More and more common for compact app.
    Extremely low cost & ultra-low-power
    Ultra-small size available (3.2×1.6×1.1mm)
    Relatively high gain
    Omni-directional radiation patterns
    Require more careful RF design : sensitive to footprint, ground plane size & keep-out area
    Respecting all recommendations does not guaranty performance due to potential detuning effects created by nearby objects

## Slide 25
Antenna Part
GNSS – Ignion DUO mXTEND (NN03-320)
  Features
    High efficiency
    Low power consumption
    Operating range : 1561 -10600 MHz
    Best for : 1561 - 5875 MHz
    Multipurpose : Multiband IoT chip antenna component with multiport (2 ports)
    No clearance beyond the antenna footprint
    Compact size : 7.0 × 3.0 × 2.0 mm
    Versatile : Device corner or center edge
    Reliability : Off-the-Shelf standard product
DUO mXTEND - Datasheet

## Slide 26
Antenna Part
GNSS – Ignion DUO mXTEND (NN03-320)
  Expected Performance
    Expected overall efficiency : 50%
    Expected overall S11 : -10dB
    Very sensitive to PCB size (ground plane)
Frequency (MHz) | 1559 | 1610 | Avg. 1559 - 1610
Total efficiency (%) | 46.3 | 46.5 | 49.2
ID | Value | Part Number | Manuf.
Z1 | 11nH | LQW18AN11NG80 | Murata
Z2 | 13nH | LQW18AN13NG80 | Murata
Z3 | 9.7nH | LQW15AN9N7G80 | Murata

## Slide 27
Hardware Part
Electrical Schematic
  …
    ….

## Slide 28
Hardware Part
LTEWatch Prototype Board (PCB)

## Slide 29
Software Part
LTEWatch Application Decomposition
U
s
e
r
I
n
t
e
r
f
a
c
e
A
c
c
e
l
e
r
o
m
e
t
e
r
D
i
s
p
l
a
y
B
u
t
t
o
n
s
&
L
E
D
s
B
T
N
0
.
.
2
L
E
D
0
.
.
2
M
o
t
o
r
s
M
0
.
.
8
D
I
S
P
_
/
E
N
D
I
S
P
_
S
C
S
S
P
I
S
P
I
A
C
C
_
C
S
A
C
C
_
/
I
N
T
P
o
w
e
r
S
u
p
p
l
y
B
a
t
t
e
r
y
L
e
v
e
l
B
a
t
t
e
r
y
C
h
a
r
g
e
r
B
A
T
_
/
I
N
T
_
C
H
R
G
B
A
T
_
L
V
L
_
E
N
I
2
C
B
A
T
_
L
V
L
R
F
&
N
e
t
w
o
r
k
G
N
S
S
R
e
c
e
i
v
e
r
L
T
E
L
T
E
_
E
X
T
_
A
N
T
G
P
S
-
R
X
D
G
P
S
-
T
X
D
/
R
S
T
I
2
C
U
A
R
T
{
G
P
S
-
E
N
E
X
T
I
N
T
D
e
b
u
g
g
i
n
g
F
T
D
I
U
S
B
_
T
X
U
S
B
_
R
X
U
A
R
T
}
S
y
s
t
e
m
M
C
U
n
R
F
9
1
6
0
6
7
2
1
0
1
8
7
5
9
5
P
0
.
2
3
P
0
.
2
4
M
A
G
P
I
O
0
P
0
.
0
P
0
.
0
C
O
E
X
0
P
0
.
2
5
M
A
G
P
I
O
1
P
0
.
0
8
-
S
D
A
P
0
.
0
9
-
S
C
L
P
0
.
1
0
P
0
.
1
1
P
0
.
1
6
-
A
I
N
3
P
0
.
2
P
0
.
2
S
C
K
-
P
0
.
3
M
O
S
I
-
P
0
.
3
P
0
.
2
P
0
.
2
P
0
.
1
3
.
.
1
P
0
.
1
7
.
.
1
P
0
.
0
.
.
P
0
.
1
3
=
>
M
2
=
>
L
E
D
2
P
0
.
1
4
=
>
M
1
=
>
L
E
D
1
P
0
.
1
5
=
>
M
0
=
>
L
E
D
0
P
0
.
0
0
=
>
M
8
P
0
.
0
1
=
>
M
7
P
0
.
0
2
=
>
M
6
P
0
.
0
3
=
>
M
5
P
0
.
0
4
=
>
M
4
P
0
.
0
5
=
>
M
3
S
D
A
S
C
L
S
S
C
L
S
D
A
S
C
L
D
A
P
0
.
1
7
=
>
B
T
N
2
P
0
.
1
8
=
>
B
T
N
1
P
0
.
1
9
=
>
B
T
N
0
M
O
S
I
S
C
K

## Slide 30
Software Part
LTEWatch Application Diagram
  Peripherals Driver (Nordic): nrfx
  Modem Driver (Nordic): nrfxlib
  RTOS: Zephyr RTOS
    RTOS
    LVGL
  Executive Framework: XF
    XFHAL / XF / PicoXF
  Hardware Abstract Layer : HAL
    BATHAL
    LEDHAL / GPIOHAL
    MOTORDRIVER HAL
  External Library (u-blox): ubxlib
  Custom Driver : Driver
    Motor Driver (HEVS)
    drv_bq25180
  Middleware
    Calendar, LED, Button, GPIO, Motor, LTE, MQTT Client
    Display Ctrl, Button Ctrl, LED Ctrl, Motor Ctrl, MQTT Ctrl, GNSS Ctrl, Battery Ctrl
  Application
    Factory, AppFactory
    PicoWatch

## Slide 31
Software Part
Software Architecture
  …
    ….

## Slide 32
Software Part
External Library
  Light and Versatile Graphics Library (LVGL)
    A fully portable C (C++ compatible) library with no external dependencies
    Can be compiled to any MCU or MPU, with any (RT)OS
    Supports monochrome, ePaper, OLED or TFT displays
    Needs only 32 kB RAM and 128 kB Flash, a frame buffer, and at least an 1/10 screen sized buffer for rendering
  u-blox Host Library (ubxlib)
    30+ built-in Widgets (Button, Label, Slider, Chart, Keyboard, Meter, Arc, Table)
    Flexible Style system with (≈100 styles)
    Flexbox & Grid-like layouts (size & position)
    Texts are rendered with UTF-8 encoding
    Word wrapping, kerning, text scrolling
    Rendering engine supporting animations, anti-aliasing, opacity, smooth scrolling, shadows, image transformation
    Supports Mouse, Touchpad, Keypad, Keyboard, External buttons
    Multiple display support

## Slide 33
Software Part
Hardware Description
  …
    ….

## Slide 34
Test & Result
LTEWatch Device
  ThingsBoard Dashboard
    GNSS position tracking on OpenStreetMap
    Number of satellites (SVS)
    Speed of the device in km/h
    Battery level in %
    Battery level in mV
    Last published altitude of the device
    Graphs of published altitude, speed, SVS and battery level values
BLOCK | SPECIFICATION | OK/KO
Power supply | Powered by a battery | OK
 | Rechargeable by USB-C and WPC | OK
 | Battery life of at least one day | OK
Data Display | Time is displayed with 3 clock hands | OK
 | LCD must be implemented | OK
User Interface | The user interface must be done with four push-buttons | OK
 | Accelerometer can be added | OK
Computing Unit | Must use the nRF9160 | OK
RF Comm. | Must implement a GNSS receiver | OK
 | Must implement an LTE-M/NB-IoT transceiver | OK
 | Must have on-board antenna for both GNSS and LTE-M | OK
 | Must have SMA connectors for GNSS and LTE-M | OK
Mechanical | Build a prototype board | OK

## Slide 35
Test & Result
GNSS & LTE-M/NB-IoT

## Slide 36
Test & Result
GNSS & LTE-M/NB-IoT

## Slide 37
Discussion
Personal Evaluation
  …
    ….

## Slide 38
Discussion
Remaining Work
  …
    ….

## Slide 39
Conclusion
  …
    ….

## Slide 40
Questions