## Slide 1
Tristan Traiber – 22.02.2022 – MSE – EIE - TIN
TM Project Defense
Analog LTE-M / NB-IoT Watch

## Slide 2
TM Project Defense - Analog LTE-M / NB-IoT Watch
Table of contents
  Introduction
    Project Description
    Scope & Limitation
  Literature Review & Research
    Wearable & Low-Power App
    System MCU (nRF9160 SiP)
    System Power Supply
    Cellular IoT & GNSS
  Results & Solutions
    Specification
    Functional Decomposition
    Component Selection
  Hardware Part
    Electrical Schematic
    LTEWatch Prototype Board
  Antenna Part
    Cellular (LTE-M/NB-IoT)
    GNSS
  Software Part
    LTEWatch Application Decomposition
    LTEWatch Application Diagram
    Software Architecture
    External Library
    Hardware Description
  Test & Result
    LTEWatch Device
    GNSS & LTE-M/NB-IoT
  Discussion
    Personal Evaluation
    Remaining Work
  Conclusion

## Slide 3
Introduction
Project Description
  About Nordic Semiconductor
    Fabless Semiconductor Company from Norway
    Specialized in wireless communication technologies and IoT
    Pioneer role in development of Bluetooth Low Energy (BLE)
    Currently developing for ANT+, Thread, Zigbee, LTE-M/NB-IoT, Wi-Fi and GSMA
  Goals & Objectives
    Develop an analog wristwatch with cellular LTE-M/NB-IoT communication and GNSS position tracking using Nordic’s nRF91 family of devices.

## Slide 4
Introduction
Scope & Limitation – Task List
  Specification
    Elaborate the specification of the device (number of clock hands, battery lifetime, user interface, size, recharging mechanism, case)
  Antenna
    Study and implement antenna solutions for both GNSS and LTE-M/NB-IoT
  Hardware
    Component selection
    Design of the schematic and PCB of a prototype
    Assembly and electrical testing of the prototype
  Software
    Develop a simple watch application that must implement motorized clock’s hands, buttons, LCD, LTE-M/NB-IoT communication using the MQTT protocol, GNSS position and time tracking, battery charging and level monitoring, accelerometer.
  Prototype validation
    Test and validation of the entire development
  Documentation
    Establish a technical report enabling further developments

## Slide 5
Introduction
Scope & Limitation – Project Constraint
  Limited Time
  Limited Resourses
    Study and implement antenna solutions for both GNSS and LTE-M/NB-IoT
  Hardware
    Component selection
    Design of the schematic and PCB of a prototype
    Assembly and electrical testing of the prototype

## Slide 6
Literature Review & Research
Wearable & Low-Power App
  …
    ….

## Slide 7
Literature Review & Research
System MCU (nRF9160 SiP)
  …
    ….

## Slide 8
Literature Review & Research
System Power Supply
  …
    ….

## Slide 9
Literature Review & Research
Cellular IoT & GNSS
  …
    ….

## Slide 10
Results & Solutions
System Specification
  …
    ….

## Slide 11
Results & Solutions
Functional Decomposition
  …
    ….

## Slide 12
Results & Solutions
Component Selection
  …
    ….

## Slide 13
Antenna Part
Cellular (LTE-M/NB-IoT)
  …
    ….

## Slide 14
Antenna Part
Global Navigation Satellite Systems (GNSS)
  …
    ….

## Slide 15
Hardware Part
Electrical Schematic
  …
    ….

## Slide 16
Hardware Part
LTEWatch Prototype Board (PCB)
  …
    ….

## Slide 17
Software Part
LTEWatch Application Decomposition
  …
    ….

## Slide 18
Software Part
LTEWatch Application Diagram
  …
    ….

## Slide 19
Software Part
Software Architecture
  …
    ….

## Slide 20
Software Part
External Library
  …
    ….

## Slide 21
Software Part
Hardware Description
  …
    ….

## Slide 22
Test & Result
LTEWatch Device
  …
    ….

## Slide 23
Test & Result
GNSS & LTE-M/NB-IoT
  …
    ….

## Slide 24
Discussion
Personal Evaluation
  …
    ….

## Slide 25
Discussion
Remaining Work
  …
    ….

## Slide 26
Conclusion
  …
    ….

## Slide 27
Questions